## Slide 1: ERTS Final Assessment – Task 2 (Template)
Kalyan Sudra – eo20203
Ronaldo Balram – nz20469
Khush Shah – bi20475
Qijia Tang – dm22509

## Slide 2: Practical elements
Show that the LED has been used effectively
Show that the robot can move around effectively
Show that the robot can play a tune
Show that all of this works simultaneously

## Slide 3: Tasks/Scheduling
We created various tasks with “taskMasterThread” having the highest priority and utilised the round robin scheduling algorithm.
With round robin at a high frequency all tasks seem to be running concurrently on a single processor.
Tasks are easily able to be suspended and resumed re-joining the schedule.
Deals with all processes without any priority

## Slide 4: Resource control
How have you controlled access to any shared data/hardware?
We have controlled access to shared data using the various tasks and the paths you take.
- bumpSwitch_status is a global variable and is being shared in the various tasks so that they are aware of the status.
We are using the dcMotor_response which uses the “status” returned from dcMotor.c which is the value returned once the robot has completed its path
There are various tasks which have been declared and we use these when we want to perform an operation for example “vTaskSuspend(taskHandle_PlaySong)” and “vTaskResume(taskHandle_PlaySong)”

## Slide 5: Suspend and Delete
What is the difference between suspend and delete task and what are their uses ?
Tasks that are deleted are removed from “all ready, blocked, suspended and event lists”. No longer able to be used. Useful to delete a task and free memory.
Suspended tasks are unable to execute unless explicitly told to meaning it can stop and resume to join the round robin schedule again